## Slide 1
Rethinking Enterprise Network Security Monitoring by Leveraging Local Processing
Prof. Vern Paxson

## Slide 2: ENTERPRISE SECURITY MONITORING: GOALS
VISIBILITY
Understand / Detect / Mitigate / Hunt for issues
requires rich analysis
requires rich data
CONTROL
Block incipient issues
requires real-time action
enhanced by richer visibility (1) in case of failures to detect (2) to more accurately control

## Slide 3: ENTERPRISE SECURITY MONITORING: ARCHITECTURE
WHAT TYPES OF DATA ARE GATHERED?
WHERE ARE
THEY GATHERED?
ANSWER: WHERE THEY’RE GENERATED...
Servers, end systems, middleboxes
How much at point of capture?
How much centrally?
WHERE IS THE DATA PROCESSED?
ANSWER:
THE MORE, THE BETTER
Network flows, web server logs, email (SMTP/IMAP) logs, LDAP, DHCP, syslog, process execution, NAT mappings, DNS, SSH login, VPN, firewall, NIDS, AV...
WHERE THEY TRAVEL (passive) network monitoring
-OR-
ANSWER: WHAT THIS TALK IS ABOUT

## Slide 4: TODAY'S PREDOMINANT ENTERPRISE SOLUTION: DATA LAKE ANALYSIS
GATHER DISPARATE LOGS …
PROCESS THERE WITH MASSIVE COMPUTER CLUSTERS
… into a centralized “data lake”
MANY OF THOSE LOGS COME FROM NETWORK DATA
⇒ How should we gather & process them?
AUTOMATED ANALYTICS PROVIDE ALERTS
⇒ Analyst explores alerts using UI / database queries

## Slide 5: THE PENDULUM OF SYSTEMS DESIGN
AS THESE CHANGE IN RELATIVE TERMS, SO DO ARCHITECTURES
e.g. mobile handsets expensive local computation, expensive communication ⇒
communication becomes cheaper ⇒ transformative for app design
e.g. cloud
IF have sufficient bandwidth ⇒ can leverage cheap remote computation
HOWEVER:
When analyzing communication itself, sending a complete copy of it elsewhere is fundamentally going to be expensive

## Slide 6
NETWORK DATA FLOOD

## Slide 7: WHEN DO WE FUNDAMENTALLY NEED “NETWORK RESIDENT ANALYSIS”

## Slide 8: WHEN DO WE FUNDAMENTALLY NEED “NETWORK RESIDENT ANALYSIS”
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET CONTENTS
e.g., extracting executables transferred over HTTP

## Slide 9: WHEN DO WE FUNDAMENTALLY NEED “NETWORK RESIDENT ANALYSIS”
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET CONTENTS
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET TIMING / HEADERS
e.g., deducing nature of encrypted traffic
e.g., extracting executables transferred over HTTP

## Slide 10: WHEN DO WE FUNDAMENTALLY NEED “NETWORK RESIDENT ANALYSIS”
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET CONTENTS
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET TIMING / HEADERS
COMPUTATION MUST COMPLETE QUICKLY
e.g., deducing nature of encrypted traffic
e.g., offloading by skipping capture of huge data transfers
e.g., extracting executables transferred over HTTP

## Slide 11: WHEN DO WE FUNDAMENTALLY NEED “NETWORK RESIDENT ANALYSIS”
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET CONTENTS
COMPUTATION REQUIRES DETAILED ANALYSIS OF PACKET TIMING / HEADERS
COMPUTATION MUST COMPLETE QUICKLY
IMPORTANT TO ALTER/REDACT INFORMATION EARLY
e.g., deducing nature of encrypted traffic
e.g., offloading by skipping capture of huge data transfers
e.g., keeping private information from entering “data lake”
e.g., extracting executables transferred over HTTP

## Slide 12: WHAT CAN WE DO WITH PROCESSING AT POINT OF NETWORK CAPTURE?
Participants, total volume, when, duration, ports (= service?) THAT’S ALL
EXPORT
NETFLOW

## Slide 13: WHAT CAN WE DO WITH PROCESSING AT POINT OF NETWORK CAPTURE?
Participants, total volume, when, duration, ports (= service?) … THAT’S ALL
Missing: web server logs, email (SMTP/IMAP) logs, LDAP, DHCP, DNS, SSH login, VPN, ...
EXPORT
NETFLOW

## Slide 14: WHAT CAN WE DO WITH PROCESSING AT POINT OF NETWORK CAPTURE?
Participants, total volume, when, duration, ports (= service?) … THAT’S ALL
Missing: web server logs, email (SMTP/IMAP) logs, LDAP, DHCP, DNS, SSH login, VPN, ...
PROS
CONS
EXPORT
NETFLOW
Lightweight network load; illuminates communication patterns
(very) Limited visibility

## Slide 15: WHAT CAN WE DO WITH PROCESSING AT POINT OF NETWORK CAPTURE?
Alerts about detections of specific problems as they occur …
… plus immediate context
PROS
CONS
EXPORT
INTRUSION DETECTION: SURICATA / FIREEYE / PALO ALTO NETWORKS / ETC.
Can find/block specific problems as they occur; very lightweight network load
Control devices ⇒ no illumination of general activity vital for subsequent investigations (incident response, forensics, threat hunting)

## Slide 16: WHAT CAN WE DO WITH PROCESSING AT POINT OF NETWORK CAPTURE?
General-purpose, in-depth packet processing for visibility
⇒
Extensive activity logs
PROS
CONS
EXPORT
conn
dce rpc
dhcp
dnp3
dns
http
files
intel
irc
mysql
notice
ntlm
sip
ssl
GENERAL NETWORK-RESIDENT ANALYSIS: BRO
Illuminates general activity;
platform for general local processing
Storage load (extensive data export); requires extensive local computation ⇒ which modern multicore systems now make feasible

## Slide 17: BRO
I began design & implementation in 1995
Basis for a bunch of research papers
$10M+ in US funding for development (bro.org)
Open-source; widely used today

## Slide 18: SOME COMPANIES USING BRO

## Slide 19: BRO
I began design & implementation in 1995
Basis for a bunch of research papers
$10M+ in US funding for development (bro.org)
Open-source; widely used today
Applies parsers (dozens) to TCP/UDP/IP traffic
  parallelizable ⇒ can do rich forms of analysis
Distills packets into higher-level events
  abstraction layer between PCAP and logs;
  provides great flexibility & extensibility
Plugs into broader architecture by exporting logs

## Slide 20: A FEW OF BRO’S LOGS

## Slide 21: BRO: MUCH MORE IS LOGGED
Logs > 400 attributes of network traffic
But: < 1% original traffic volume

## Slide 22: IT’S NOT JUST ABOUT PROTOCOL PARSING
E.g. “stepping stone” detection finding linked SSH sessions through which attackers relay traffic
Done via fine-grained packet timing analysis, w/o contents
Infeasible to do other than locally due to v. high volume of traffic to inspect
INFERENCES ABOUT ENCRYPTED STREAMS:
SURGICAL REMOVAL OF SENSITIVE INFORMATION:
Can transform / strip out sensitive information from log entries...
  e.g., personal identifiers, bank account numbers
  e.g., privacy: anonymize information at point of collection
... before it enters the data lake
To do so at point of network capture requires detailed context to soundly identify such data ⇒ rich processing

## Slide 23: IT’S NOT JUST ABOUT DATA VOLUME
NETWORK-RESIDENT ANALYSIS IS FUNDAMENTALLY MORE TIMELY THAN DATA-LAKE ANALYSIS CAN BE
ENABLES COORDINATION WITH OTHER REAL-TIME SENSING
ENABLES REACTIVE RESPONSE
ENABLES DYNAMIC ADAPTATION OF THE CAPTURE PROCESS ITSELF
e.g., communicate with firewall to kill connection quicker ⇒ less damage
e.g., analysis across many connections • DDoS mitigation
• scan detection ⇒ blocking
e.g., communicate with end-systems to determine processes & users associated with sockets

## Slide 24: DYNAMIC ADAPTATION ENABLES EXTREMELY HIGH-SPEED MONITORING
PACKET CAPTURE
MONITORING
Flows
Shunted
flow
Shunting: supports extremely high-speed network monitoring by directly forwarding high-volume flows once determined to be safe
Decisions must be made in milliseconds to be effective

## Slide 25: ENTERPRISE NETWORK SECURITY MONITORING BY LEVERAGING LOCAL PROCESSING
1
NETWORK MONITORING PROVIDES EXTENSIVE MUST-HAVE INFORMATION ABOUT ENTERPRISE ACTIVITY
2
ABSENCE OF SUFFICIENT CAPACITY TO MIRROR ALL OF THE TRAFFIC TO CENTRAL DATA LAKE REQUIRES RICH NETWORK-RESIDENT ANALYSIS
3
EVEN IF CAPACITY EXISTS, LATENCY REQUIREMENTS STILL REQUIRE NETWORK-RESIDENT ANALYSIS
4
A POWERFUL, EXTENSIBLE TOOL FOR SUCH ANALYSIS: BRO
Real-time coordination, reactive blocking, dynamic adaptation
Facilitating real-time detection, incident analysis, forensics, threat-hunting
vern@corelight.com

## Slide 26
THANKS

## Slide 27: BIOGRAPHY
DR. VERN PAXSON
Vern Paxson is a Professor at UC Berkeley, and co-founder and Chief Scientist of Corelight, a company based on the “Bro” network monitoring technology he has developed for many years. His research focuses heavily on measurement-based analysis of network activity and Internet attacks. He works extensively on high performance network monitoring, detection algorithms, cybercrime, and countering censorship and abusive surveillance. He has received the ACM SIGCOMM Award, the Grace Murray Hopper Award, and the IEEE Internet Award.
Reach him at vern@corelight.com, vern@berkeley.edu

## Slide 28: OVERVIEW
RETHINKING ENTERPRISE NETWORK SECURITY MONITORING BY LEVERAGING LOCAL PROCESSING
Modern architectures for enterprise security monitoring focus heavily on ingesting vast, disparate sensing information - logs and alerts from all sorts of processes and devices - into central data stores. Sites then employ a range of analytics over the consolidated data to identify and respond to security issues. A key question for such architectures is whether to rely solely on centralized data processing, or if some forms of processing might be more effectively done locally where the sensing occurs. In this talk I'll develop the powerful possibilities of employing rich local processing: efficiently distilling traffic into high-level behaviors; inferring activity cloaked in encrypted streams; coordinating with other sensors; dynamically adapting the capture and analysis process; reactive blocking; and scrubbing out highly sensitive information to keep it from ever entering the central data store.